## Slide 1
UNDERWATER NOISE MEASUREMENT
Enoc Martínez Padró

## Slide 2
TABLE OF CONTENTS
01
INTRODUCTION
Ocean Sound and
Underwater Noise

## Slide 3
OCEAN SOUND
NATURAL SOURCES
Marine mammals
Fish swarms
Wind and waves
Earthquakes
Thermal sound

## Slide 4
OCEAN SOUND

## Slide 5
OCEAN SOUND
ANTHROPOGENIC SOURCES
Shipping
Seismic exploration
Sonar
Offshore energy
…
UNDERWATER NOISE
Anthropogenic sound harmful to the marine environment

## Slide 6
UNDERWATER NOISE

## Slide 7
UNDERWATER SOUND
OCEAN SOUND TRENDS
Increase of about 3 dB/decade
(northeastern Pacific at 40 Hz)
WORLD’S FLEET

## Slide 8
UNDERWATER NOISE

## Slide 9
UNDERWATER NOISE
Source: Slabbekoorn, Hans, et al. "A noisy spring: the impact of globally rising underwater sound levels on fish." Trends in ecology & evolution 25.7 (2010): 419-427.
Hildebrand, John A. "Anthropogenic and natural sources of ambient noise in the ocean." Marine Ecology Progress Series 395 (2009): 5-20.

## Slide 10
MASKING
Source: Slabbekoorn, Hans, et al. "A noisy spring: the impact of globally rising underwater sound levels on fish." Trends in ecology & evolution 25.7 (2010): 419-427.
Hildebrand, John A. "Anthropogenic and natural sources of ambient noise in the ocean." Marine Ecology Progress Series 395 (2009): 5-20.

## Slide 11
MSFD
MARINE STRATEGY FRAMEWORK
DIRECTIVE (MSFD)
European Union Directive
Aims to achieve a “good environmental status” (GES)
Defines 11 descriptors
Including underwater noise
Picture courtesy of EMODnet Chemistry (www.emodnet-chemistry.eu)

## Slide 12
TABLE OF CONTENTS
02
HYDROPHONES AND
OBSERVATION PLATFORMS

## Slide 13
HYDROPHONES
Complex sensor systems
Measure underwater sound
Very high data volume
Highly heterogeneous
Deployment strategies
Standalone (hydrophone + batteries)
  Internal recordings
  No real-time communications
Integrated into observation platforms
  ↑ Spatial coverage
  ↑ Autonomy
  ↑ Real-time communications
HYDROPHONES

## Slide 14
OBSERVATION PLATFORMS
OBSERVATION PLATFORMS
Stations/vehicles that host sensors
Fixed or mobile
Provide power and telemetry
Highly heterogeneous
USUAL CONSTRAINTS
Power availability
Bandwidth (satellite, RF, …)
Computational resources
INTRODUCTION

## Slide 15
OBSERVATION PLATFORMS

## Slide 16
HYDROPHONE INTEGRATION
HYDROPHONE INTEGRATION
Acoustic Recordings (WAV)
  Up to tens of GB / day
  Not RT data via GSM/Satellite
  Large on-board storage required

## Slide 17
HYDROPHONE INTEGRATION
HYDROPHONE INTEGRATION
Acoustic Recordings (WAV)
  Up to tens of GB / day
  Not RT data via GSM/Satellite
  Large on-board storage required
In Situ Processing
  Few KB / day → real-time delivery
  On-board signal processing
  Computational resources

## Slide 18
TRANSMISSION SAVINGS
T snapshot (s) | Volume (KB / day) | Tx energy (MJ) | Battery (% / day)
1 | 8640 | 0.3024 | 1.78
10 | 864 | 0.03024 | 0.18
20 | 432 | 0.01512 | 0.09
60 | 144 | 0.00504 | 0.03
300 | 28.8 | 0.001008 | 0.01
Sampling (kHz) | Volume (GB / day) | Tx energy (MJ) | Battery (% / day)
2 | 0.35 | 12.25 | 72.06
6 | 1.04 | 36.4 | 214.12
24 | 4.15 | 145.25 | 854.41
96 | 16.59 | 580.65 | 3415.59
192 | 33.18 | 1161.3 | 6831.18
SEAGLIDER
Battery capacity: 17 MJ1
Telemetry: Satellite (Iridium)
Telemetry cost: 35 J/Kbyte2
Hydrophone: 16 bit
TX PROCESSED DATA
TX RAW HYDROPHONE DATA
1 www.kongsberg.com
2 Rudnick, Daniel L., et al. "Underwater gliders for ocean research." Marine Technology Society Journal 38.2 (2004): 73-84.

## Slide 19
HYDROPHONE INTEGRATION

## Slide 20
TABLE OF CONTENTS
03
UNDERWATER NOISE
ALGORITHMS

## Slide 21
Contribution: Interoperable Architecture
Based on standards
Any sensor (including hydrophones)
Any observation platform
Apply to Passive Acoustics
Demonstrate feasibility
In situ processing
Use Case: MSFD Descriptor
11.1 Impulsive Sounds
11.2 Continuous low-frequency sound
OCEAN SOUND
Picture courtesy of EMODnet Chemistry (www.emodnet-chemistry.eu)

## Slide 22
CONTINUOUS LOW-FREQUENCY SOUND
Different metrics can be used
  Best practices
  MSFD Specifications
Sound Pressure Level (SPL)
Third-octave frequency bands:
  63 Hz, 125 Hz
  10 Hz – 20 kHz (optional)
Time snapshot (10 – 60 secs)
OCEAN SOUND
(and 2 kHz)

## Slide 23
SPL ALGORITHMS
Spectral
Analysis
Filter
Bank
FFT
Goertzel
Algorithm
Temporal
Analysis
SPL over 1/3 octave bands

## Slide 24
TEMPORAL ANALYSIS
T
Pressure (µPa)
Time (s)
Pressure (µPa)
Time (s)
97.54 dB re µPa
FILTER BANK
Decimating (sampling rate↓↓)
Apply band-pass filter
SPL equation (temporal)
Once filter per band
Filter
Filter
Bank
FFT
Goertzel

## Slide 25
TEMPORAL ANALYSIS
T
Pressure (µPa)
Time (s)
Pressure (µPa)
Time (s)
97.54 dB re µPa
85.32 dB re µPa
FILTER BANK
Decimating (sampling rate↓↓)
Apply band-pass filter
SPL equation (temporal)
Once filter per band
Filter
Filter
Bank
FFT
Goertzel

## Slide 26
SPECTRAL ANAYSIS
Pressure (µPa)
Time (s)
T
Frequency (s)
PSD
97.54 dB re µPa
85.32 dB re µPa
91.83 dB re µPa
FAST FOURIER TRANSFORM
DFT optimized for N = 2M
Estimate PSD using FFT
Select bands of interest
Integrate frequency bands
Filter
Bank
FFT
Goertzel

## Slide 27
SPECTRAL ANAYSIS
Pressure (µPa)
Time (s)
T
Frequency (s)
PSD
97.54 dB re µPa
85.32 dB re µPa
91.83 dB re µPa
GOERTZEL’S ALGORITHM
DFT (slower than FFT)
Individual DFT terms
Only bands of interest
SPL in frequency domain
Filter
Bank
FFT
Goertzel

## Slide 28
ALGORITHM COMPARISON
SPL ALGORITHM COMPARISON
Compare algorithm performance to obtain
SPL level:
  Filter Bank
  FFT
  Goertzel
Parameters to evaluate:
  Execution time
  RAM memory used
Test conditions:
  Increase time snapshot T (Δf = fs/N)
  Increase third-octave bands

## Slide 29
TABLE OF CONTENTS
04
USE CASES

## Slide 30
OBSEA
Name | OBSEA
Platform type | Cabled Observatory
Telemetry | Ethernet
Location | Vilanova i la Geltrú
Processing | Real-time / Server
Sensor Interfaces | UDP

## Slide 31
EGIM
Name | EGIM
Platform type | Datalogger / mooring
Telemetry | None
Location | Taliarte (Gran Canaria)
Processing unit | PC (offline)
Sensor Interfaces | UDP, Serial

## Slide 32
OBJECTIVE 3
Name | SeaExplorer
Platform type | Underwater glider
Telemetry | Iridium
Location | Norway
Processing unit | Real-time / uC
Sensor Interfaces | RS232
SEAEXPLORER GLIDER

## Slide 33
THANK YOU FOR YOUR ATTENTION